Arm Pi Corresponding Items
Pin mapping

Purpose	Raspberry Pi pins		Purpose	Raspberry Pi pins		Purpose	Raspberry Pi pins
Servo7	GPIO5		Servo8	GPIO6		Servo1	GPIO12
Servo6	GPIO13		UART TX	GPIO14		UART RX	GPIO15
Servo2	GPIO16		IO Port RX	GPIO17		Servo5	GPIO19
Servo3	GPIO20		Servo4	GPIO21		KEY2	GPIO22
LED2	GPIO23		LED1	GPIO24		KEY1	GPIO25
IO Port TX	GPIO27

The default use of each LED light and button

Component	Purpose	Explanation
LED1	Display the working state	Flash once in every two second
LED2	Display the connecting state of Wi-Fi	Flash in direct connection mode, keep lighting in LAN mode,
KEY1	Reset the Wi-Fi	Long press the LED2 in LAN mode until it goes out to clear the Wi-Fi account and password and turn the connection method to the connection mode. Its no uses indirect connection mode
KEY2	Shut down the system	Long press it for 3 seconds (or until LED1 and LED2 stop flashing), to shut down the Pi. When the shutdown stop, LED1 and LED2 will enter the dark flashing state. Then, when the green LED on raspberry pie will stage flashing and goes out, at this state, you can turn off the power supply